## Slide 1: EDA Story – ML IoT Independent Study
Bryan Nsoh

## Slide 2: Big Picture
  Goal: forecast volumetric water content (VWC) to automate irrigation decisions for LoRaWAN-connected plots
  Deliver 20–25 min walkthrough of messy field data → modeling → failure analysis
  Focus on single notebook VWClstm-daily-injection.ipynb + SQLite store processed_data.db
  Present every design decision, rationale, and outcome transparently

## Slide 3: Data Context
  Source: data_table in Archive/processed_data.db (37 704 rows, July 19 – Oct 13, 2023)
  36 plots, hourly telemetry (weather, canopy temp, irrigation totals, four VWC depths)
  Target depths used: 6“, 18”, 30“; 42” discarded after quality review
  Short seasonal window ⇒ only ~11 weeks of signal per plot; must squeeze learning from dense feature stack

## Slide 4: Initial Audit
  Missingness: irrigation often zero; VWC sensors occasionally flatline or spike
  Duplicate timestamps resolved via drop_duplicates() prior to indexing
  Hourly cadence mostly consistent (≈1 080 samples per plot subset)
  Takeaway: model must tolerate sparse irrigation events and noisy soil probes

## Slide 5: Cleaning Pipeline
  Trim leading/trailing NaN runs with trim_start_end_nans
  Resample daily for visualization, but keep hourly data for modeling
  PCHIP interpolation to fill interior gaps without step artefacts
  Savitzky–Golay smoothing (window = 20) to suppress probe noise without lagging events

## Slide 6
Cleaning pipeline

## Slide 7: Feature Engineering
  Spike flags: VWC_*_spike_up/down capture ±15 % day-to-day jumps
  Irrigation history: time_since_last_significant_precip, time_since_last_half_max_precip, rolling 7-day cumulative
  Log transform + binary flag for irrigation to boost rare-event visibility
  Mean-centering + first-difference derivatives for each VWC depth before scaling

## Slide 8: Reduced Feature Set
  After cuts: 17 continuous + 3 VWC targets + 3 VWC derivatives + irrigation flag
  Drops include: categorical crop/growth stage (sparse), VWC_42 (noisy), redundant weather extrema combinations
  Scaling via buffered MinMaxScaler preserves future headroom (±30 %)

## Slide 9: Training Workflow
  Sliding window: 7-day input (168 hourly steps) → 4-day horizon (96 hourly steps)
  TimeSeriesSplit (5 folds) intended for cross-plot validation, but bug feeds only first plot’s folds → limited generalization
  LSTM stack: 512→256→128→128→64 with dropout + L2; Dense reshaped to horizon × targets
  Early stopping on mean fold MSE; best weights saved in LSTM_dayhour/

## Slide 10: Model Behaviour – Plot 2003
Pred vs actual – Plot 2003

## Slide 11
- Captures overall decay/trend but underestimates irrigation rebounds - Surface layer (6") best aligned; deeper probes drift shortly after forecast window starts

## Slide 12: Model Behaviour – Plot 2014
Pred vs actual – Plot 2014

## Slide 13
- Systematic positive bias on 6" depth → likely due to limited drydown examples in training folds - 18“/30” profiles miss the sharp post-irrigation peak entirely

## Slide 14: Model Behaviour – Plot 2015
Pred vs actual – Plot 2015

## Slide 15
- Model follows trend but lags actuals by ~2 days; deeper probe diverges once soil drains - Highlights dataset imbalance: this plot irrigated more aggressively than training plots

## Slide 16: Injection Experiment
Injection sweep

## Slide 17
- Synthetic irrigation (+0.25, +0.5, +1.0) applied just before forecast - Desired outcome: higher predicted VWC correlating with injection size - Observed: predictions nearly flat; averages barely change across injections

## Slide 18: Why Irrigation Fails
  Injection added after scaling ⇒ engineered features (precip_irrig_log, flags, rolling sums) unchanged, starving the network of irrigation cues
  Adding 0.25–1.0 to the scaled feature pushes it beyond training range (MinMax [0,1]), inducing distribution shift the LSTM never saw
  Training bug reused folds from the first plot only, so the model never learned cross-plot irrigation variability; unseen responses default to trend continuation

## Slide 19: Lessons Learned
  Cleaning pipeline solid, but engineered irrigation features must update whenever interventions occur
  Fix fold selection to ensure each plot contributes to training/validation
  Re-inject irrigation prior to scaling and recompute transforms to test sensitivity honestly
  Future modelling: consider hybrid physics constraints or attention on precipitation signals

## Slide 20: Next Steps
  Rebuild training workflow with correct fold splitting + data augmentation on irrigation events
  Create automated figure scripts (post-analysis) to regenerate slides as data evolves
  Package notebook narrative into live demo for Q&A on transformation choices