## Slide 1: Enhancing Irrigation Water Management through Integration of Internet of Things (IoT) and Machine Learning (ML) Techniques
Bryan Nsoh, Graduate research assistant
University of Nebraska-Lincoln

## Slide 2: Background
Importance and motivation for the study
Identification of knowledge gaps

## Slide 3: Problem Statement
Rising pressure on groundwater resources from climate change
Additional stress on the already burdened High Plains Aquifer
Need for efficient water-to-yield conversion to support the growing population
Notes: High Plains Aquifer: A study highlights that in parts of the High Plains, groundwater resources are being rapidly depleted, compromising food security The research uses a model to predict reductions in groundwater withdrawal and subsequent declines in crop production For Nebraska, the model projects grain production to continue rising through 2050 due to high recharge rates, suggesting a relatively more sustainable situation compared to states like Texas (Mrad et al, 2020)
Impact of Climate Change: Climate change is also affecting groundwater availability and irrigation in the Republican River Basin, which is part of the US High Plains aquifer The study predicts that both groundwater pumping and recharge will increase, but the effects of pumping will dominate, leading to more pronounced declines in groundwater levels in areas with irrigation-driven decreasing trends (Ou et al, 2018)
Overall Water-Level Changes: A report on the High Plains aquifer indicates that water-level changes from predevelopment to recent years have included substantial declines in some areas The area-weighted average water-level changes in the aquifer showed an overall decline, indicating a net loss of groundwater over several decades (McGuire, 2011)

## Slide 4: Challenges in optimizing AG water management
Lack of real-time, end-to-end systems for ag-water monitoring at scale
Need for interpretable, reliable predictive modelling to aid water use recommendations backed by live weather, plant and soil data

## Slide 5: Research Objectives
Objective 1: Design of IoT scalable, low cost Platform that can integrate different sensor, datalogger and connections protocol types in low cost fashion and manage high data volumes
Objective 2: Design ML Algorithm that can integrate diverse data sources and metrics and combine their insights and synergies to accurately model sol and plant dynamics

## Slide 6: Hypothesis
Hypothesis 1: An optimal, scalable IoT system will facilitate data-driven insights and integration of a wider suite of sensors
Hypothesis 2: An Ml system that makes use of a more diverse array of data and metrics will make more accurate irrigation scheduling decisions

## Slide 7: Materials & Methods
Real Time Data collection and processing
Predictive modeling using LSTM

## Slide 8: Field Layout
Sensor and node details:
  TDR Sensors installed at depths of 6, 18, 30, and 42 inches.
  Mounted IRT sensor, maintained at 1 meter above canopy height.
  Dendrometer sensor placed around plant stem
  Nodes equipped with Campbell CR-800 data loggers and raspberry pi with a lora hat.
Notes: Say ET method, soil moisture sensor scheduling and IOT, each of these had 3 reps in both corn adn soybeans

## Slide 9: Location Overview: University of Nebraska-Lincoln West Central Research, Extension, and Education Center
Coordinates: Lat 411° N, Long 1008° W
Climate: Precipitation 21" (early summer), Temp: Summer 80s F, Winter 10s F
Soil: Cozad Silt Loam (Organic Matter 088%, Clay 16%, Sand 356%, Silt 484%, Slope 0-3%, pH 64)
Groundwater: Ogallala Aquifer (Depth 8-12 ft)
Experiment: IoT, 1 Replication, 3 Treatments
Red: Corn, Yellow: Soybean
Notes: Show nodes in image with starts or something. can be estimate

## Slide 10: DATA COLLECTION & pROCESSING

## Slide 11: Data Collection System Overview
1
2
3
1
2
3

## Slide 12: Data Collection hARDWARE - Dataloggers
Managed by Raspberry Pi 4
PiSupply Lora Hat for Lora Transmission
Linovision Lorawan Gateway
12V, 14Ah Lithium batteries
30W solar panels
2 Data Logging options

## Slide 13: Field to Cloud: Data Collection
Sensors collect data every 30 minutes
Local processing on Raspberry Pi
LoRa transmission to gateway
MQTT broker aggregates field data
Real-time data streaming enabled

## Slide 14: Cloud Functions Workflow
Weather data: OpenWeatherMap API (current and 4-day forecast)
Mesonet API: local high-precision weather data
Cloud Scheduler triggers functions periodically
CWSI, ET_ref, SWSI computed on schedule
Data insertion function triggered by PubSub messages
All results stored in BigQuery for analysis

## Slide 15: Fuzzy Logic for irrigation Scheduling

## Slide 16: Introduction
Traditional approach uses fixed thresholds; fuzzy logic allows for gradual transitions
Fuzzy logic captures real-world imprecision in irrigation decisions (e.g., "somewhat dry" soil)
Better mimics human expert reasoning for complex environmental factors

## Slide 17: Fuzzy System Components and Process
Inputs: SWSI (Soil Water Stress Index), CWSI (Crop Water Stress Index), ET (evapotranspiration) - key environmental factors
Fuzzification: Convert precise input values into degrees of membership in fuzzy sets
Rule base and inference: Apply expert knowledge to fuzzy inputs, determining irrigation needs
Defuzzification: Convert fuzzy conclusions into a precise irrigation amount
Output: Final recommended irrigation quantity

## Slide 18: Fuzzification and Membership Functions
Converting crisp inputs (e.g., SWSI of 0.7) to fuzzy values (e.g., 70% 'dry', 30% 'normal’)
Overlapping functions allow smooth transitions, reflecting real-world ambiguity in categories
Linguistic variables like "dry" or "wet" capture human-like reasoning about water conditions
Fuzzy Rules and Inference
Rules use IF-THEN structure to encode expert knowledge about irrigation decisions
Multiple rules can fire simultaneously, each contributing to the final decision
Rule strength depends on the degree of membership of input values in rule conditions

## Slide 19: DETERMINING THE STRENGTH OF EACH RULE
Crisp inputs are fuzzified into degrees of membership in input fuzzy sets
Each rule is evaluated using these fuzzified inputs
For rules with multiple conditions (e.g., IF A AND B THEN C):
  Use the minimum of individual condition strengths
  Example: IF CWSI is 'high_stress' (0.7) AND SWSI is 'dry' (0.8) THEN strength = min(0.7, 0.8) = 0.7
The resulting strength is applied to the rule's consequent (output) fuzzy set
This process is repeated for all rules in the system
Rule: IF CWSI is 'high_stress' AND SWSI is 'dry' THEN irrigation is 'high'

## Slide 20: Defuzzification
Aggregating rule outputs: Combine all activated rules into a single fuzzy output set
Centroid method finds the "balance point" of the aggregated fuzzy set
This balance point becomes the crisp (precise) irrigation amount recommendation

## Slide 21: Cloud to Analysis: Data Processing
VM forwarder prepares data for cloud
Google Cloud PubSub for scalable messaging
Cloud Functions process incoming data
BigQuery stores and enables complex analytics
Scheduled functions compute irrigation metrics

## Slide 22: Cloud to Analysis: Data Processing
VM forwarder prepares data for cloud
Google Cloud PubSub for scalable messaging
Cloud Functions process incoming data
BigQuery stores and enables complex analytics
Scheduled functions compute irrigation metrics

## Slide 23: Cloud to Analysis: Data Processing
VM forwarder prepares data for cloud
Google Cloud PubSub for scalable messaging
Cloud Functions process incoming data
BigQuery stores and enables complex analytics
Scheduled functions compute irrigation metrics

## Slide 24: Cloud to Analysis: Data Processing
VM forwarder prepares data for cloud
Google Cloud PubSub for scalable messaging
Cloud Functions process incoming data
BigQuery stores and enables complex analytics
Scheduled functions compute irrigation metrics

## Slide 25: Conclusions and Future Work
IoT system successfully integrates diverse sensors
LSTM model shows promise for soil moisture prediction
Challenges in capturing irrigation effects
Future: Expand dataset, refine feature engineering
Potential for real-time irrigation decision support

## Slide 26: THANK YOU!

## Slide 27: ML MODELS FOR VWC PREDICTION

## Slide 28: LSTM Model Architecture
Deep learning for irrigation prediction
5 LSTM layers (512 to 64 units)
Dropout and Batch Normalization for regularization
Dense layer output: 4 days x 3 targets
Optimized for soil moisture prediction

## Slide 29: Data Preprocessing for LSTM
Daily resampling of 15-min data (reduce noise, capture daily patterns)
Savitzky-Golay filter: smoothing (preserves features better than moving average)
Log transform for precipitation (handle skewed distribution)
Time-based features: cyclical encoding (capture seasonal patterns)
Sequence creation: 7-day input, 4-day forecast (balance history and future prediction)
PCHIP interpolation for missing values (preserves shape of time series)

## Slide 30: Time Series Cross-Validation
Multiple datasets, same time period (Jul-Sep 2023)
5-fold chronological split
Train on 4 folds, validate on 1
Simultaneous validation across datasets
Preserves temporal order of data

## Slide 31: LSTM Training Process
Custom training loop implementation
Adam optimizer with initial LR: 0.001
Learning rate decay after 15 epochs
Early stopping: patience of 200 epochs
Loss function: Mean Squared Error

## Slide 32: Model Performance on Test Set
Input window: 7 days
Prediction window: 4 days
Sliding forward prediction
Metrics: RMSE, MAE for each soil depth
Comparison with baseline models

## Slide 33: Model Performance on Test Set
Input window: 7 days
Prediction window: 4 days
Sliding forward prediction
Metrics: RMSE, MAE for each soil depth
Comparison with baseline models

## Slide 34: Irrigation Injection Simulation
Injection amounts: 0, 0.25, 0.5, 1 inch
Injected at end of input sequence
Prediction horizon: 4 days post-injection
Model showed limited sensitivity to injection
Possible reasons: data sparsity, feature dominance